## Slide 1
Build Your Own Garden Shed
Community workshop, session 2
Framing the walls and roof

## Slide 2
What we build today
2
• Four wall frames, studs at 400 mm
• Door opening 800 x 1700
• Rafters at 600 mm, 30 degree pitch
• Ridge board and collar ties

## Slide 3
Timber needed
3
Item | Section (mm) | Length (mm) | Qty
Studs | 45 x 70 | 1820 | 26
Plates | 45 x 70 | 2400 | 4
Side plates | 45 x 70 | 1710 | 4
Rafters | 45 x 95 | 1480 | 8
Ridge board | 25 x 120 | 2600 | 1

## Slide 4
Time per stage (hours, two people)
4
Chart: 
| Base | Wall frames | Raise and brace | Roof framing | Roof boards and felt | Cladding | Door
Hours | 3 | 4 | 1.5 | 3 | 2.5 | 5 | 2

## Slide 5
Safety in the workshop
5
• Eye and ear protection on the saw bench
• Two people to lift and raise each wall
• Clamp work before cutting
• Keep the floor clear of offcuts