## Slide 1
Community Library: Design Concept
Concept design presentation
Site, programme and sustainability

## Slide 2
Site plan
2

## Slide 3
Programme areas
3
Chart: 
| Adult collection | Children and teens | Study rooms | Community hall | Staff and back of house | Circulation
m2 | 420 | 310 | 160 | 220 | 140 | 200
Space | m2
Adult collection | 420
Children and teens | 310
Study rooms (8) | 160
Community hall | 220
Staff and back of house | 140
Circulation | 200
Total | 1450

## Slide 4
Design principles
4
• A single generous reading room under a timber roof, lit from north-facing clerestories
• Children's area opens onto the reading garden
• Community hall with its own entrance for evening use
• Mass timber structure on a concrete ground floor
• All-electric building with heat pumps and rooftop solar

## Slide 5
Energy targets (kWh/m2 per year)
5
Chart: 
| Heating | Cooling | Lighting | Equipment | Hot water | Solar offset
Typical library | 62 | 18 | 28 | 22 | 6 | 0
This design | 21 | 9 | 9 | 18 | 3 | -24